This page was exported from All The Latest MCTS Exam Questions And Answers For Free Share [    https://www.mctsdump.com    ]

Export date: Wed Apr 17 21:17:08 2024 / +0000 GMT

## [July-2016 Dumps] Do Not Miss 400-101 Exam Dumps Shared By PassLeader -- 100% Exam Pass Guarantee

New Updated 400-101 Exam Questions from PassLeader 400-101 PDF dumps! Welcome to download the newest PassLeader 400-101 VCE dumps: http://www.passleader.com/400-101.html (1119 Q&As)

Keywords: 400-101 exam dumps, 400-101 exam questions, 400-101 VCE dumps, 400-101 PDF dumps, 400-101 practice tests, 400-101 study guide, 400-101 braindumps, CCIE Routing and Switching Written Exam

P.S. Free 400-101 dumps download from Google Drive: https://drive.google.com/open?id=0B-ob6L_QjGLpfnRCUEFYcEhWZUw3OGNQY2FUSkptUXBrZDVzeE8zdkJQUERtOUFINDBFQW8

NEW QUESTION 1070

A network engineer is extending a LAN segment between two geographically separated data centers. Which enhancement to a spanning-tree design prevents unnecessary traffic from crossing the extended LAN segment?

A.    Modify the spanning-tree priorities to dictate the traffic flow.

B.    Create a Layer 3 transit VLAN to segment the traffic between the sites.

C.    Use VTP pruning on the trunk interfaces.

D.    Configure manual trunk pruning between the two locations.

Answer: C

NEW QUESTION 1071

The OSPF database of a router shows LSA types 1, 2, 3 and 7 only. Which type of area is this router connected to?

A.    backbone area

B.    totally stubby area

C.    stub area

D.    not-so-stubby area

Answer: D

NEW QUESTION 1072

Which feature can you implement to most effectively protect customer traffic in a rate-limited WAN Ethernet service?

A.    HCBWFQ

B.    IntServ with RSVP

C.    DiffServ

D.    The IPsec VTI qos pre-classify command

E.    Q-in-Q

Answer: A

NEW QUESTION 1073

An engineer has configured a router to use EUI-64, and was asked to document the IPv6 address of the router. The router has the following interface parameters:

mac address C601.420F.0007

subnet 2001:DB8:0:1::/64

A.    2001:DB8:0:1:C601:42FF:FE0F:7

B.    2001:DB8:0:1:FFFF:C601:420F:7

C.    2001:DB8:0:1:FE80:C601:420F:7

D.    2001:DB8:0:1:C601:42FE:800F:7

Answer: A

NEW QUESTION 1074

Which command configures port security on a switch to enable permanent MAC address learning on the interface?

A.    switchport port-security mac-address-learning enable

B.    switchport port-security mac-address timer 0

C.    switchport port-security mac-address sticky

D.    switchport port-security mac-address maximum 1 sticky

E.    switchport port-security mac-address permanent

Answer: C

NEW QUESTION 1075

If EIGRP and OSPF are configured within an administrative domain for the same network, which value can you change so that the OSPF becomes the installed routing protocol for all routes?

A.    Local preference

B.    Metric

C.    MED

D.    Administrative distance

E.    Prefix length

Answer: E

NEW QUESTION 1076

Which three components are in an MPLS header? (choose three)

A.    a 4-bit experimental use field

B.    a 4-bit label stack entry

C.    an 8-bit TTL

D.    a 2-bottom of stack

E.    a 3-bit experimental use field

F.    a 20-bit label

Answer: CEF

NEW QUESTION 1077

What is the main function of VRF-lite?

A.    To allow devices to use labels to make Layer 2 Path decisions

B.    To segregate multiple routing tables on a single device

C.    To connect different autonomous systems together to share routes

D.    To route IPv6 traffic across an IPv4 backbone

Answer: B

NEW QUESTION 1078

Refer to the exhibit. Which prefixes will have their distance changed?

router eigrp 100

network 10.0.0.0

distance 80  10.1.12.0  0.0.0.255  10

!

access-list 10 permit 10.1.0.0  0.0.255.255

A.    all prefixes matching access-list 10 learned from peers in the range 10.1.12.0- 10.1.12.255

B.    all internal prefixes in the range 10.1.12.0-10.1.12.255 learned from peers matching access-list 10

C.    all internal prefixes matching access-list 10 learned from peers in the range 10.1.12.0- 10.1.12.255

D.    all prefixes in the range 10.1.12.0-10.1.12.255 learned from peers matching access-list

Answer: C

NEW QUESTION 1079

Which two methods do IPsec VTIs used to identify and transmit encrypted traffic through the tunnel? (choose two)

A.    static routing

B.    dynamic routing

C.    object groups

D.    ACLs

E.    NAT

Answer: AB

NEW QUESTION 1080

When you deploy DMVPN, what is the purpose of the command crypto isakmp key ciscotest address 0.0.0.0 0.0.0.0 ?

A.    It is configured on hub and spoke router to establish peering

B.    It is configured on hub to set the pre-shared key for the spoke routers

C.    It is configured on the spokes to indicate the hub router

D.    It is configured on the Internet PE routers to allow traffic to traverse the ISP core

Answer: B

NEW QUESTION 1081

……

Download the newest PassLeader 400-101 dumps from passleader.com now! 100% Pass Guarantee!

400-101 PDF dumps & 400-101 VCE dumps: http://www.passleader.com/400-101.html (1119 Q&As)

P.S. Free 400-101 dumps download from Google Drive: https://drive.google.com/open?id=0B-ob6L_QjGLpfnRCUEFYcEhWZUw3OGNQY2FUSkptUXBrZDVzeE8zdkJQUERtOUFINDBFQW8

Post date: 2016-07-13 10:22:55

Post date GMT: 2016-07-13 10:22:55

Post modified date: 2016-07-13 10:22:55

Post modified date GMT: 2016-07-13 10:22:55

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com