This page was exported from All The Latest MCTS Exam Questions And Answers For Free Share [    https://www.mctsdump.com    ]

Export date: Tue Apr 16 18:17:17 2024 / +0000 GMT

## [Apr-2016 Dumps] Learning PassLeader 200-355 Free VCE and PDF Dumps To Pass Exam Quickly

New Updated 200-355 Exam Questions from PassLeader 200-355 PDF dumps! Welcome to download the newest PassLeader 200-355 VCE dumps: http://www.passleader.com/200-355.html (410 Q&As)

Keywords: 200-355 exam dumps, 200-355 exam questions, 200-355 VCE dumps, 200-355 PDF dumps, 200-355 practice tests, 200-355 study guide, 200-355 braindumps, Implementing Cisco Wireless Network Fundamentals Exam

NEW QUESTION 377

What is the effect of increasing antenna gain on a radio?

A.    focusing energy in a defined direction

B.    adding energy creating a larger cell

C.    aligning phase shifting

D.    improving frequency specific diversity

Answer: B

NEW QUESTION 378

Which signal strength reading indicates that the engineer is closest to the access point?

A.    -43 dBm

B.    -67 dBm

C.    -87 dBm

D.    -100 dBm

Answer: A

NEW QUESTION 379

The new tablets for the sales department require an SNR of 18 or more to operate. Given a noise floor of - 88 dBm, what is the minimum RSSI that is needed?

A.    -60 dBm

B.    -70 dBm

C.    -72 dBm

D.    -80 dBm

E.    -96 dBm

F.    -106 dBm

Answer: B

NEW QUESTION 380

Refer to the exhibit. A network engineer needs the far end of a wireless bridge to receive at -45dBM.

Based on the diagram, what value in dBm must the transmitter use to send to achieve the desired result?

A.    -118

B.    -28

C.    -20

D.    20

E.    28

F.    118

Answer: E

NEW QUESTION 381

Refer to the exhibit. A wireless engineer has an antenna with the radiation pattern shown in the exhibit. What type of antenna is it?

A.    Patch

B.    Yagi

C.    Parabolic dish

D.    Dipole

E.    Internal omni

Answer: B

NEW QUESTION 382

When reading a radiation pattern for an antenna, at which two drops in signal and power is the beamwidth measured? (Choose two.)

A.    3 dB

B.    6 dB

C.    9 dB

D.    10 dB

E.    1/2 power

F.    1/4 power

G.    1/8 power

H.    1/10 power

Answer: AE

NEW QUESTION 383

When calculating the link budget for a wireless point-to-point bridge, the engineer notices that one antenna has its gain marked as 2.85 dBd. With a 20-mW access point and 3-dBi loss for the cable, what is the approximate EIRP?

A.    15 dBm

B.    18 dBm

C.    22 dBm

D.    25 dBm

Answer: A

NEW QUESTION 384

Due to the terrain, a deployment requires a point-to-point wireless bridge to allow for network connectivity to a remote building. What 5GHz band would permitted to use the highest power in the U.S.?

A.    U-NII-3

B.    U-NII-2 Extended

C.    U-NII-2

D.    U-NII-1

Answer: A

NEW QUESTION 385

A wireless engineer is designing a network for the London branch of a company. Which 5-GHz band allows the branch to use the highest EIRP?

A.    2.4-GHz ISM

B.    UNII-1

C.    UNII-2

D.    UNII-2 Extended

Answer: D

NEW QUESTION 386

......

Download the newest PassLeader 200-355 dumps from passleader.com now! 100% Pass Guarantee!

200-355 PDF dumps & 200-355 VCE dumps: http://www.passleader.com/200-355.html (410 Q&As)

Post date: 2016-04-19 04:37:31

Post date GMT: 2016-04-19 04:37:31

Post modified date: 2016-04-19 04:37:31

Post modified date GMT: 2016-04-19 04:37:31

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com