This page was exported from All The Latest MCTS Exam Questions And Answers For Free Share [    https://www.mctsdump.com    ]

Export date: Thu Apr 18 7:29:31 2024 / +0000 GMT

## [June-2016 Dumps] Real 400-101 Exam Questions -- All People Need To Learn For Not Failing Exam

New Updated 400-101 Exam Questions from PassLeader 400-101 PDF dumps! Welcome to download the newest PassLeader 400-101 VCE dumps: http://www.passleader.com/400-101.html (1069 Q&As)

Keywords: 400-101 exam dumps, 400-101 exam questions, 400-101 VCE dumps, 400-101 PDF dumps, 400-101 practice tests, 400-101 study guide, 400-101 braindumps, CCIE Routing and Switching Written Exam, v5.0

NEW QUESTION 988

Which three service offer VLAN transparency for WAN Ethernet services? (Choose three)

A.    ERMS

B.    EPL

C.    ERS

D.    MPLS

E.    EMS

F.    EWS

Answer: ABC

NEW QUESTION 989

Which two values are required to implement an EIGRP named configurations? (Choose two)

A.    address-family

B.    process-id

C.    subnet-mask

D.    virtual-instance-name

E.    router-id

Answer: AB

NEW QUESTION 990

What are the two EEM event subscribers? (Choose two)

A.    CLI

B.    script

C.    applet

D.    none

E.    syslog

Answer: BC

NEW QUESTION 991

How is a targeted LDP session different from a standard LDP session?

A.    Targeted LDP is used only for neighbors on different segments.

B.    Targeted LDP requires SDP to be enabled.

C.    Targeted LDP requires RSVP to be enabled.

D.    Targeted LDP uses unicast hello messages to peer with other devices.

Answer: D

NEW QUESTION 992

Which two options are valid IPV6 extension header typers? (Choose two)

A.    Flow Label

B.    Encapsulating security Payload

C.    Version

D.    Traffic Class

E.    Mobility

Answer: BE

NEW QUESTION 993

Your NetFlow collector is not working due to a large amount of traffic entering your network which is destined to a single IP address. Which NetFlow feature allows you to collect the top source hosts for this traffic on the local router?

A.    A NetFlow can export flows only to a extermal flow collector

B.    show ip cache flow

C.    ip accounting

D.    ip flow-top-talkers

Answer: D

NEW QUESTION 994

For which reason can two OSPF neighbor routers on the same LAN segment be stuck in the two-way state?

A.    The two routers have different MTUs on the interface.

B.    The two routers are configured with different priorities.

C.    The interface priority is set to zero on both routers.

D.    Both routers have the same OSPF router ID.

Answer: C

NEW QUESTION 995

……

NEW QUESTION 997

Which information is contained in an OSPF Type 1 Router LSA?

A.    The Autonomous System Border Routers(ASBR) for the OSPF network and the cost of the path to reach each ASBR

B.    The router's interfaces(links) on which OSPF is enabled ,the state and outgoing cost of each link.and the OSPF neighbors on each link

C.    The network links to all known OSPF routers and and the cost of each path

D.    The Area Border Routers (ABR) for the area and the cost of the path to each ABR

E.    The OSPF neighboring routers and the cost of the outgoing link to reach each neighbor

Answer: B

NEW QUESTION 998

Which command can you enter to configure a built-in policer with minimum guaranteed bandwidth without starving other classes during periods of congestion?

A.    bandwidth remaining percent

B.    bandwidth

C.    priority percent

D.    fair-queue

Answer: C

NEW QUESTION 999

Which three session tables does NAT64 maintain?

A.    6rd

B.    TCP

C.    484XLAT

D.    ICMP Query

E.    SIP

F.    UDP

Answer: BDF

NEW QUESTION 1000

Which two statements about Cisco Express Forwarding load balancing are true?

A.    Cisco Express Forwarding can load-balance over a maximum of two destinations

B.    It combines the source IP address subnet mask to create a hash for each destination

C.    Each hash maps directly to a single entry in the RIB

D.    Each hash maps directly to a single entry in the adjacency table

E.    It combines the source and destination IP addresses to create a hash fdor each destination

Answer: DE

NEW QUESTION 1001

……

Download the newest PassLeader 400-101 dumps from passleader.com now! 100% Pass Guarantee!

400-101 PDF dumps & 400-101 VCE dumps: http://www.passleader.com/400-101.html (1069 Q&As)

Post date: 2016-06-08 10:35:17

Post date GMT: 2016-06-08 10:35:17

Post modified date: 2016-06-08 10:35:17

Post modified date GMT: 2016-06-08 10:35:17

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com